## Slide 1
Multiobjective Bayesian optimization for online accelerator tuning
JKPS 250321
21, Mar 2025
Minseo Jeong

## Slide 2
2
JKPS 250321
Index
Background
Multi-objective Bayesian Optimization(MOBO)
Optimization of AWA photoinjector

## Slide 3
Background
JKPS 250321
3

## Slide 4
Optimization
JKPS 250321
4
Optimization: Finding xmin in domain Ω such that xΩ f(xmin)≤f(x)(f is objective function)
For accelerator, optimizing every objective parameter is impossible due to space charge, etc
If x1 is no worse than x2 for all objectives and x1 is better than x2 in at least one objective, then x1 dominates x2
Pareto front(PF): Set of non-dominant solutions in objective space
Hypervolume: Size of the portion of the objective space that is dominated by the PF

## Slide 5
Optimization
JKPS 250321
5
Grid search: Evaluates f at points separated by a fixed step in each direction
- takes long time
Random search: Evaluates f at randomly chosen points
- does not guarantee the best solution

## Slide 6
Optimization
JKPS 250321
6
Evolutionary algorithm: An optimization algorithm based on evolutionary operators, such as recombination and mutation
Y. Li et al. Phys. Rev. Accel. Beams 21. (2018).

## Slide 7
Optimization
JKPS 250321
7
Bayesian optimization(BO): Model-based optimization algorithm using probability distribution model based on previous observations
Bayes’ theorem:
Let B be prediction model, and A be measurement, then
posterior
likelihood
prior

## Slide 8
Multi-objective Bayesian Optimization
JKPS 250321
8
R. Roussel et al. Phys. Rev. Accel. Beams 27. (2024).
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 9
Multi-objective Bayesian Optimization
JKPS 250321
9
Advantage: Sample efficient, robust to noise, incorporation of prior information
- Efficient when objective function is expensive to evaluate
Disadvantage: Computational complexity(O(n3)), assumption of smoothness, inefficient if objective function is simple and cheap to evaluate
- Unable to use in high dimensional (10~20) space

## Slide 10
Multi-objective Bayesian Optimization
JKPS 250321
10
Gaussian process(GP): the surrogate model which represents function value at random input variable via multivariate Gaussian distribution
- f(x) ∼ GP[μ(x), k(x,x’)]
Kernel(k(x,x’)): a function which represents covariance between two input points
-
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 11
Multi-objective Bayesian Optimization
JKPS 250321
11
For an arbitrary observation point x*:
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 12
Multi-objective Bayesian Optimization
JKPS 250321
12
Commonly used kernel:
-Radial basis function()
-Matérn function: generalized version of RBF kernel
is modified Bessel function of second kind, ν=3/2 or 5/2)
If objective function is periodic, using periodic kernel can be an option
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 13
Multi-objective Bayesian Optimization
JKPS 250321
13
Length scale hyperparameter l should be optimized by maximizing marginal log-likelihood(MLL)
- log p(y|X, θ)= −yTK-1 yy/2-log |Ky| −n/2 log 2π
R. Roussel et al. Phys. Rev. Accel. Beams 27. (2024).
Notes: θ is the set of GP model hyperparameters
The first term is the data fit term which is maximized when model predictions accurately predict experimental data.
The second term describes model complexity and is maximized given the simplest model,
The final term is a normalization constant based on the number of training points in the dataset.
IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 14
Multi-objective Bayesian Optimization
JKPS 250321
14
Acquisition function: the function that determines which input point to measure next
Exploitation: focuses on the vicinity of current best measurement points
Exploration: focuses on unexplored region
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 15
Multi-objective Bayesian Optimization
JKPS 250321
15
Expected Improvement(EI): an acquisition function that indicates expected increment of function
-
(Φ and φ are the probability distribution function and cumulative distribution function of a
Gaussian distribution)
R. Roussel et al. Phys. Rev. Accel. Beams 27. (2024).
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 16
Multi-objective Bayesian Optimization
JKPS 250321
16
Upper confidence bound (UCB): an acquisition function which explicitly specifies the trade-off between exploration and exploitation
-
- β can be increased during the process to avoid sticking in local optimum
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 17
Multi-objective Bayesian Optimization
JKPS 250321
17
Expected Hypervolume Improvement(EHVI):
-
(r is reference point, is multivariate Gaussian probability distribution function)
- Required computational cost increases exponentially to the dimension of objective space
Upper confidence bound hypervolume improvement(UCB-HVI): an acquisition function which explicitly specifies the trade-off between exploration and exploitation
-
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 18
Multi-objective Bayesian Optimization
JKPS 250321
18
Started with a set of five random input points
Kernel: RBF with l=1.0, =0.5
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 19
Multi-objective Bayesian Optimization
JKPS 250321
19
Preference treatment: specifies that the optimizer searches in a given objective subspace
(e.g. )
Constraint: multiplies the acquisition function the probability that the constraint will be satisfied
(
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 20
Multi-objective Bayesian Optimization
JKPS 250321
20
Proximal input space exploration: modifing the acquisitionfunction so that each optimization step travels a small distance in parameter space during optimization
(x0: recently observed point in input space,
Λ: matrix that specifies cost associated with changing input parameter)
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 21
Optimization of AWA Photoinjector
JKPS 250321
21
Parameters of AWA photoinjector(photogun+one RF cavity) was optimized
A. Edelen et al., Phys. Rev. Accel. Beams 23, 044601 (2020)
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 22
Optimization of AWA Photoinjector
JKPS 250321
22
Kernel: RBF with initial hyperparameter vector l
- Hyperparameter optimization is done by maximizing the log marginal likelihood of the GP model with the gradient based Adam optimization algorithm, with 5000 iterations and a learning rate of 0.001
- l is updated with period of 10 turns
Acquisition function: UCB-HVI with β=0.01
Method of maximizing the acquisition function : particle swarm optimization
Notes: PSO: 각각의 입자들이 가진 정보와 종합적인 정보를 종합하여 각각의 입자의 다음 위치를 선정
-계산량이 많지만, 전체적으로는 global optimum에 수렴 가능
IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 23
Optimization of AWA Photoinjector
JKPS 250321
23
MOBO was 35 times more efficient than NSGA-II
Took 45 min to optimize
Since neither NSGA-II nor I-NN includes a direct calculation of the hypervolume increase for each proposed observation point, hypervolume generated by MOBO is larger than others
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 24
Optimization of AWA Photoinjector
JKPS 250321
24
Preference/constraint of dE<0.52MeV was set
(b) MOBO with an optimization preference of dE < 0.52 MeV.
(c) MOBO with an inequality constraint of dE < 0.52 MeV
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 25
Optimization of AWA Photoinjector
JKPS 250321
25
Proximal optimization with Λ=4I was demonstrated
Change of K1 parameter is mirrored in each of the other five input parameters
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 26
Conclusion
JKPS 250321
26
MOBO is ideal tool for online multiobjective accelerator optimization
MOBO can be repeated periodically to monitor changes in machine performance over time
Advanced method can be applied in MOBO in order to reduce optimization time
(e.g. q-EHVI, multi-fidelity modeling, trust-region Bayesian optimization(TuRBO)
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 27
Conclusion
JKPS 250321
27
MOBO is ideal tool for online multiobjective accelerator optimization
MOBO can be repeated periodically to monitor changes in machine performance over time
Advanced method can be applied in MOBO in order to reduce optimization time
(e.g. q-EHVI, multi-fidelity modeling, trust-region Bayesian optimization(TuRBO)
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 28
Thank you!
JKPS 250321