## Slide 1: Data-Based Condition Monitoring and Disturbance Classification in Actively Controlled Laser Oscillators
Arne Grünhagen, Annika Eichler, Marina Tropmann-Frick, Görschwin Fey

## Slide 2: European X-ray Free Electron Laser
@ Deutsches Eletronen Synchrotron (DESY)
Linear particle Free Electron Laser producing intense, ultrashort X-ray pulses.
Source: European XFEL GmbH
Source: European XFEL GmbH

## Slide 3: Laser-based Synchronization System
@EuXFEL
detector
optical synchronization
Pump Probe Experiments
Femtosecond synchronization between accelerator and PPL.
Laser Oscillator generates the synchronizing signal.
Links between laser oscillator and synchronized devices each are actively length-stabilized.
electrons
X-ray beam
Source: European XFEL GmbH

## Slide 4: Laser-based Synchronization System
@EuXFEL
No pump-probe experiments possible if laser-based synchronization does not work at high performance.
Main component of the system: laser oscillator
  216.667 MHz signal (4.6 ns)
  Synchronization of other components via a stable phase
Synchronizing signal is influenced by different disturbances:
  Changes in the environment (temperature, humidity, air pressure, vibrations)
  Electrical, optical, mechanical
  Seismic activities
Active phase stabilization using Proportional Integral (PI) controller.
PI - controller
controller output
phase error
disturbances

## Slide 5: Pipeline
Goal: Comparison of Feature Extraction and Diagnosis Methods
Controller Output
Phase error
Feature Extraction
Data Preparation
Input: | CTRL output and phase error
Output: | time snippet and PSD
Input: | time snippet and PSD
Output: | feature vector
Diagnosis
Input: | feature vector
Output: | Assignment of disturbance classes at any time with certainty score

## Slide 6: Data Preparation
Welch’s Method
Spectral Density Estimation using Welch’s method.
PSD reveals power distribution of a signal across different frequencies.
  Identify dominant frequencies.
  Detect periodic or noise components in a signal.

## Slide 7: Feature Extraction
Statistics
Calculate a set of basic characteristics using from time snippet and PSD.
13 statistics are calculated for each time snippet or PSD.
time (sec) | maximum | minimum | mean | standard deviation | variance | …
0.0 – 0.1 | -89.0351 | -114.0734 | -109.8984 | 2.3916 | 5.7201 | …
0.1 – 0.2 | -88.9563 | -113.9317 | -109.9277 | 2.3566 | 5.5538 | 
… |  |  |  |  |  | 
Example: statistics from PSD

## Slide 8: Feature Extraction
Peak Characteristics
Peaks are important characteristics of a PSD
Peak features
  Most prominent peaks
  Number of peaks having a minimum prominence per range. Each range covers 5000 kHz.
time (sec) | Peak 1 - prominence | Peak 1 - Hz | Peak 1 - power | …
0.0 – 0.1 | 30,23 | 60,322 | -99,36 | …
0.1 – 0.2 | 30,23 | 60,289 | -99,29 | …
… | … | … | … | …
Example: peak characteristics from PSD

## Slide 9: Feature Extraction
Autoencoder
Autoencoder is trained on 2500 dimensional PSDs.
10-dimensional latent space is used as feature vector.
time (sec) | latent 0 | latent 1 | …
0.0 – 0.1 | -0.5923 | 0.1238 | …
0.1 – 0.2 | -0.5303 | 0.0166 | …
… | … | … | …
Example: autoencoder feature extraction

## Slide 10: Fault Detection, Fault Classification
Detection (19 algorithms)
Semi supervised learning: compare unknown new data with known healthy data
Clustering algorithms (4)
  Data samples are grouped into categories with similar elements
Outlier detection algorithms (15)
  Identify rare items that differ significantly from most of the other items
Classification (4 algorithms)
supervised learning: fault/disturbance classes must be known
For each fault class, the classifier assigns a feature vector to the fault class with the maximum likelihood
Feature vector of 0.1 s data
Detection
Classification
Evaluation | 
Class | Certainty
healthy | health score
type 1 | class 1 score
type 2 | class 2 score
… | …

## Slide 11: Experimental Evaluation
Acoustical Disturbance of a Laser Oscillator (Laboratory Environment)
Dataset
Disturbed frequencies: 0.5 kHz, 1.0 kHz, 1.5 kHz, …, 4.5 kHz
4 different intensity levels
30 s of data for each combination of disturbed frequency and intensity level
60 s of data with no acoustical disturbance
laser oscillator
loudspeaker
Experiment Description
Sounds are played with individual frequencies with different intensities on a surface loudspeaker next to a laboratory laser oscillator

## Slide 12: Model Evaluation
Performance Criteria
Inference duration
  Feature extraction, fault detection and fault classification for a 0.1 s data snippet must be below 0.1s.
Prediction quality
  Area Under the Receiver Operating Characteristic (AUROC) score and Accuracies
Different hyperparameters were systematically selected for each algorithm.

## Slide 13: Results: Detection
Clustering
Outlier Detection
Inference Duration
for a selection of many neighbors (>80) ABOD needs more than 0.1 sec per sample.
All algorithms with good prediction results have an inference time < 0.001 s per 0.1 s data sample.

## Slide 14: Results: Classification
Inference Duration
SVM on statistics of PSDs is the slowest with 0.0024s for a 0.1s data sample.
The other combinations require less than 0.0001s per 0.1s data sample.

## Slide 15: Conclusion & Future Work
Goal
Comparison of existing methods to detect and classify acoustical disturbances influencing the performance of laser oscillators.
Experimental Evaluation
Simulation of one specific failure type for an experimental laser setup.
Peak detection works so well because that's exactly what we generate with the experiment
Disturbances and faults during real operation are not so easy to detect.
In real operation, peaks and changes in PSDs indicate different disturbances and causes of faults.
Ongoing Work
Apply the evaluated pipeline to operational data from different laser setups.
Changes to the configuration of the setup causes previously trained diagnostic models to become invalid.

## Slide 16: Thank you.
Arne Grünhagen
Arne.Gruenhagen@desy.de Arne.Grunhagen@haw-hamburg.de
Check the paper:
https://ebooks.iospress.nl/volumearticle/66251

## Slide 17: Statistics

## Slide 18: Algorithms
Clustering

## Slide 19: Algorithms
Outlier Detection

## Slide 20: Hyperparameters
Algorithm | Parameter | Values
Birch | threshold | 0.2, 0.4, …, 3.8, 4.0
 | branching factor | 20, 40, 60, 80, 100
CBLOF | # clusters | 2, 3, 4, 5, 6, 7, 8, 9, 10, 15
 | alpha | 0.5, 0.6, 0.7, 0.9
 | beta | 1.5, 2, 5, 7, 10, 15
GMM | # components | 2, 3, 4, 5, 6, 7, 8, 9, 10, 15
K-means | # clusters | 2, 3, 4, 5, 6, 7, 8, 9, 10, 15
Algorithm | Parameter | Values
KDE | bandwidth | 0.4, 0.6, …, 2.0, 2.2
KPCA | # components | 1,2, …, 10
MCD | - | -
PCA | # components | 1,2, …, 10
Sampling | - | -
Algorithm | Parameter | Values
ABOD | # nearest neighbors | 5, 10, …, 95, 100
COF | # nearest neighbors | 5, 10, …, 95, 100
COPOD | - | -
ECOD | - | -
IOF | - | -
KNN | # nearest neighbors | 5, 10, …, 95, 100
LMDD | - | -
LOF | # nearest neighbors | 5, 10, …, 95, 100
OCSVM | - | -
SOS | perplexity | 5, 10, …, 95, 100