## Slide 1: structure wakefield acceleration for Short-pulse RF research at the Argonne Wakefield Accelerator (AWA) facility
JOHN POWER
On behalf of the AWA group
Nov, 2024
https://www.anl.gov/awa

## Slide 2: What is Short-pulse RF acceleration?
Conventional acceleration: Accelerating structure powered by an RF klystron. Pulse length: 100 ns < trf < 10 us
Advanced acceleration: Accelerating structure powered by a beam-driven SWFA. Pulse length: trf < 10 ns
Conventional acceleration
1000 ns
Accelerator Structure
drive beam
main beam
Power Extraction and Transfer Structure (PETS) driven structure
Accelerator Structure
RF Klystron Driven Structure
10 MW
10 ns
1000 MW
Structure Wakefield Acceleration (SWFA)
Why?
Higher acceleration gradients to lead to compact accelerators

## Slide 3: outline
Argonne Wakefield Accelerator (AWA) Facility
Structure Wakefield Acceleration
Short-Pulse RF High Gradient Accelerators

## Slide 4
Structure wakefield acceleration at The
Argonne wakefield accelerator
facility

## Slide 5: What are the Advanced acceleration concepts (AAC) in the U.S.?
AAC ~ Wakefield Acceleration: Laser Wakefield Acceleration, Plasma Wakefield Acceleration, and Structure Wakefield Acceleration (SWFA).
Beam Test Facilities: Demonstrating the viability of emerging accelerator science ultimately relies on experimental validation.
DLA
(Dielectric Laser Accelerator)
Energy Source
Laser pulse
Particle beam
Medium
Plasma
Structure
LWFA
(Laser WF Accelerator)
PWFA
(Plasma WF Accelerator)
SWFA
(Structure WF Accelerator)
RF Driven Structure
AWA

## Slide 6: WHERE is the AAC program in the U.S.?
AAC ~ Wakefield Acceleration: Laser Wakefield Acceleration, Plasma Wakefield Acceleration, and Structure Wakefield Acceleration (SWFA).
Beam Test Facilities: Demonstrating the viability of emerging accelerator science ultimately relies on experimental validation.
U.S. advanced and novel accelerator beam test facilities
[C. Clarke et al 2022 JINST 17 T05009, https://iopscience.iop.org/article/10.1088/1748-0221/17/05/T05009 ]
National Laboratories
Universities
BELLA
ELL
UT3
Laser Beam
FAST/IOTA
AWA
FACET-II
Particle Beam
ATF

## Slide 7: Argonne wakefield accelerator (AWA)
Argonne Campus: 15 minutes west of Chicago
AWA: HEP test facility
APS: BES national user facility
ATLAS: NP national user facility
300 AREA
400 AREA
200 AREA
Notes: Accelerators at Argonne

## Slide 8: The Argonne Wakefield Accelerator (AWA) Facility
A Beam Test Facility to enable the development of novel acceleration technology
Drive RF Photoinjector (65 MeV)
  single bunch: 100nC
  bunch train: 600 nC
Argonne Cathode Test Stand (2-4 MeV)
Cathode research and diagnostics
Physics of high-gradient breakdown
Witness RF photoinjector (15 MeV)
Provides two-beam capability
Bright beams for low-energy experiments
Experimental Switchyard
Highly reconfigurable
6D phase space manipulation
Laser
100 mJ (IR), 10 mJ (UV),
300 fs – 6 ps (UV)
temporal shaping
https://www.anl.gov/awa
8/30

## Slide 9: The Argonne Wakefield accelerator
The AWA Facility
Witness
Drive
AWA Bunker
AWA Vacuum and Experimental Zones
ACT
EXPERIMENTAL AREA
Zones 2-5 are experimental areas
Zones 2, 4, and 5 have ~ 1 m experimental area
Zones 3A & 3B are fully re-configurable
5 Zones
https://www.anl.gov/awa

## Slide 10: Developing Next-Generation Accelerator technology at the AWA
BASIC RESEARCH
3 THEMES (next slide)
DEVELOPING APPLICATIONS
    NEAR-TERM (e.g. UED)
    MID-TERM (e.g. Compact XFEL)
    LONG-TERM (e.g. linear collider)
enabling GV/m STRUCTURE WAKEFIELD acceleration to produce bright GeV-class electron beams at the Argonne Wakefield accelerator

## Slide 11: AWA facility: 3 Research themes
research themes
11
Beam Production
Electron sources
  High-brightness
  High-intensity
e.g. RF Photoinjector
Beam Manipulation
Beam shaping & control.
Beam Diagnostics.
e.g. Double Emittance Exchange
Advanced Accelerator
SWFA & PWFA
  High-Gradient
  High-Efficiency
e.g. SWFA
Long-term
Multi-TeV e+e- linear collider
      Higg’s Factory
    Mid-term
1 GeV Water-window FEL
5 GeV XFEL light sources
Inverse Compton sources
Near-term
*Compact accelerators for societal applications
Industrial
Security
Medical
Applications

## Slide 12: e-beam Driven Structure Wakefield Acceleration (SFWA)
Collinear Wakefield Acceleration
(CWA)
DB
MB
PWFA-like
A. Zholents, et al, NIMA 829, 190-193 (2016)​
A. Zholents, et al, Proceedings of IPAC2018​
main beam
drive beam
Klystron-like
CLIC CDR​: https://project-clic-cdr.web.cern.ch/CDR_Volume1.pdf​
W. Gai, C. Jing, J.G. Power, JPP 78, 339-345 (2012)​
drive beam
main beam
Power Extraction and Transfer Structure (PETS)
Accelerator
Two Beam Acceleration (TBA)
SWFA XFEL
IP
e-
e+
3TeV
1
10
1
10
SWFA 3 TeV linear collider

## Slide 13
High Gradient Operation
13/30
drive beam
main beam
Power Extraction and Transfer Structure (PETS)
Accelerator
Two Beam Acceleration

## Slide 14: Limits to high gradient operation
RF Breakdown  main problem
Field emission/dark current (unwanted beam loading and ionizing radiation can blind beam diagnostics, etc.)
Excessive conditioning time
Structure (most studied):
X-band, NCRF, 100ns<pulse length<1000 ns, OFE Copper BDR = 1e−6 m-1
RF Breakdown guidelines
Esurf < 250 MV/m,
Pulse heating: DT < 50 0C,
Power: abs(Sc) < 5 MW/mm2
Stored Energy: U < 1 J
Simakov, Dolgashev, Tantawi, “Advances in high gradient normal conducting accelerator structures, NIMA, Volume 907, 2018, https://doi.org/10.1016/j.nima.2018.02.085
14/30

## Slide 15: 3 promising paths to higher gradients
Material: Hard bi-metallic alloy (SLAC: Cu:Ag 0.8% Ag)
Temperature: cryogenic temp (SLAC/UCLA/LANL: cold copper)
1
2
3
Short RF pulse
(ANL/Tsinghua/PSI)
15/30
Notes: Not exhaustive list …

## Slide 16: The Short Pulse RF Advantage
3
3e−7/m, 100 MV/m, 200ns
Scaling Law
H. H. Braun, et al., “High-power testing of 30 GHz accelerating Structures at CTF II”, CLIC Note 475
W. Wuensch, et al., “A demonstration of high-gradient acceleration”, PAC’03
Short pulse < 100 nsec
PSI: 90 nsec TW gun
Tsinghua: Short ~50 nsec
AWA/Euclid/NIU: Ultrashort ~10 nsec
New physics? Empirical scaling law, underlying mechanism may change
Challenges: Challenges to operate in the short-pulse regime: broadband couplers, efficiency, stability, etc.
A. Grudiev, S. Calatroni, and W. Wuensch
Phys. Rev. ST Accel. Beams 12,102001 (2009)
S. Doebert et al.,PAC’05
https://accelconf.web.cern.ch/p05/PAPERS/ROAC004.PDF
klystron
TBA
1 ms
0.1 ms
long pulse regime
CLIC 2003
16/30
RF Pulse length (ns)

## Slide 17
RF power generation: PETS*
*this could also be klystron driven but needs to be short-pulse.
drive beam
main beam
Power Extraction and Transfer Structure (PETS)
Accelerator
Two Beam Acceleration
17/30

## Slide 18: short pulse rf generation at the awa
TBA drive beam PETS
…
ZONE1
ZONE3a
…
magnets & diagnostics
Drive bunch train
-5 GW beam power
-100A, 6 nsec
1.3 GHz Drive gun (Cs2Te photocathode)
  High charge bunch train (up to 600 nC)
  Final beam energy: ~65 MeV
……..
(Drive RF photoinjector)
(PETS)
Short RF pulse
(2 Hz)
Harmonics of 1.3 GHz
7.8 GHz
11.7 GHz
26 GHz
91 GHz
182 GHz
18/30
Notes: X-band test has become a general capability of AWA (work underway for 26 GHz to THz)

## Slide 19: Producing Short pulse rf power (I)
---towards 1 GW by Dielectric X-band PETS
Physics design
Mechanical design
Fabrication
J. Shao, et al, PRAB 23, 011301 (2020)
Dielectric X-band PETS (200 MW)

## Slide 20: Producing Short pulse rf power (II)
Beam
Backward Port
Forward Port
80 MW  380 MW  565MW
X. Lu, et al, PRL 122, 014801 (2019)
X. Lu, et al, APL Appl. Phys. Lett. 116, 264102 (2020)
---towards 1 GW by Metamaterial PETS
J. Picard et al., PRAB 25, 051301 (2022)

## Slide 21: PETS results at AWA (summary)
Dielectric X-band PETS (200 MW)
DOI: 10.1103/PhysRevAccelBeams.23.011301
2000 2005 2010 2015 2020 2025
1000 MW
900 MW
800 MW
700 MW
600 MW
500 MW
400 MW
300 MW
200 MW
100 MW
0 MW
C-band
dielectric
(2000)
C-band
dielectric
(2008)
X-band dielectric (2018)
X-band metallic (2018)
X-band metallic (2020)
X-band MTM (2019)
X-band MTM (2021)
AWA energy upgrade
15 MeV  65 MeV
K-band dielectric (2010)
J. Picard et al., PRAB 25, 051301 (2022)
MTM X-band PETS (565 MW)
  Highest peak power as 565 MW from a train of eight bunches with a total charge of 355 nC
Metallic X-band PETS (400 MW)
J. Shao et. al., https://accelconf.web.cern.ch/ipac2019/papers/MOPRB069.pdf
21/30

## Slide 22
TBA: high-gradient structures: accelerator
drive beam
main beam
Power Extraction and Transfer Structure (PETS)
Accelerator
Two Beam Acceleration
22/30

## Slide 23: High gradient structure test stand
Beam on YAG1
…
…
ZONE1
(Drive RF photoinjector)
ZONE3a
(PETS)
Example:
X-band gun beamline
high gradient test stand
23/30

## Slide 24
~100 MV/m Dielectric Disk Accelerator
High-power test results
AWA drive gun limited run to 293 nC
PETS = 222 MW
Gradient ~78 MV/m (no arcing, no multipactor)
Previous: 100 MV/m single cell DDA
Next: Multicell DDA
Clamped structure, like single cell.
Special attention to triple junction design
24/30

## Slide 25: ~200 MV/m Metamaterial Accelerator
Efficient structure design to explore gradient limitation
  190 MV/m peak gradient from 115 MW input RF
  11.7 GHz structure optimized for 6 ns FWHM RF pulses extracted from the drive beam
  Breakdown Insensitive Accelerating Regime (BIAR)
D. Merenich, X. Lu et al., Phys. Rev. Accel. Beams 27, 041301 (2024)
https://journals.aps.org/prab/abstract/10.1103/PhysRevAccelBeams.27.041301

## Slide 26: ~300 MV/m Iris loaded accelerator
11.7 GHz structure
Breakdown Insensitive Acceleration Regime
Drive beam
PETS
RF
400 MW RF power generated from PETS with 450 nC drive beam
300 MV/m gradient in the middle cell, 500 MV/m peak surface field
300 MV/m gradient

## Slide 27: ~400 MV/m X-band photogun
Sub-GV/m acceleration for bright beam
Xgun 
W.H.Tan et. al., PRAB 2022
Phys. Rev. Accel. Beams 25, 083402, August 2022 (2022)
400 MV/m on cathode
G. Chen et al., (AAC 2024)
Submitted to NIMA (2024)
  388 MV/m on the photocathode
  BDR ~4e-6 (estimated)
  Ultra low dark current (<1pC per RF pulse)
First photoelectron beam
Gun performance 

## Slide 28: ~700 MV/m beam-driven THz wakefield structure (planned)
>1 GW THz power
<1 GV/m gradient
EUV/IR generation
- Total : 10 m
6~7 m
Drive beam source
(20 nC, 40 MeV)
THz Accelerating Tube
THz Gun
Gun
Linac (~40 MeV)
QMs
THz Power Extraction Tube
Power Transfer
Undulator
THz Acc (700 MV/m)
THz PET (~4GW)
~2 m
~1 m
~1 m
Planned Demo Beamline
Korea Univ. Sejong: S.-H. Park, J. Ko, B.-H. Oh, H. Shim, M. K. Seo, K.-H. Kim
Norther Illinois Univ. : G. Ha
Argonne National Lab: J. Power, G. Chen, E. Wisniewski, S. Doran, W. Liu
Pohang Accelerator Lab. : J. H. Kim, H. Kong, H. J. Kwak, J. Kim, S.-H. Kim
Korea-4GSR, KBSI : S.H. Shin
First beam test
COLLABORATION
KU-PAL-NIU-ANL

## Slide 29: HIGH GRADIENT ACCELERATING STRUCTURES
Dielectric Loaded Accelerator (DLA)
2000 2005 2010 2015 2020 2025
400 MV/m
350 MV/m
300 MV/m
250 MV/m
200 MV/m
150 MV/m
100 MV/m
50 MV/m
0 MV/m
C-band TBA
DLA (2000)
K-band TBA DLA (2018)
X-band metallic (2018)
X-band metallic (2021)
AWA energy upgrade
15 MeV  65 MeV
X-band TBA DDA (2022)
X-band PC Gun (2021)
W-band CWA metallic (2015)
C-band TBA
DLA (2008)
C-band CWA
PBG (2009)
X-band MTM (2023)
Single-cell Dielectric
Disk Accelerator (DDA)
3-cell Disk Loaded Waveguide
1.5 cell X-band Photocathode Gun
Single-cell Disk Loaded Waveguide
Metamaterial Accelerator
29/30

## Slide 30
  Power Extraction and Transfer Structure (PETS)
  X-band RF test stand (500 MW, 2 Hz)
  200 MW dielectric PETS
  400 MW metallic PETS
  565 MW metamaterial PETS
  Accelerator
  High-gradient structures
  100 MV/m X-band dielectric disk accelerator
  200 MV/m X-band MTM accelerator
  300 MV/m X-band metallic accelerator
  400 MV/m X-band photocathode gun
    Discovery of BIAR regime
30/30
Summary  SWFA: SHORT-PULSE REGIME
ONGOING
Power Extraction and Transfer Structure (PETS)
Accelerator
Structure Wakefield Acceleration

## Slide 31
30/30
Summary  SWFA: SHORT-PULSE REGIME
Near term Demonstrators
10 MeV Upgrade Xgun and Xlinac
100 MeV high-brightness Xgun photoinjector beamline
Upgrade AWA drive beam energy from 65 MeV to ~130 MeV
500 MeV demonstrator
Mid to Long Applications
1 GeV water window FEL
5 GeV XFEL
Multi-TeV linear collider
NEXT STEPS

## Slide 32
extras

## Slide 33: applications
XFEL (X-ray Free electron laser)
  Coherent 42 keV X-rays ala MaRIE (e Matter-Radiation Interactions in Extremes” style)
  Using high energy (12 GeV) TBA X- & K-band linac
ICS (Inverse Compton Scattering)
  Incoherent X-rays (10’s of keV photon bursts for material studies)
  Using medium energy (30 MeV) TBA X-band linac
UED (Ultrafast Electron Diffraction)
  Pump-probe methos yields information on the dynamical changes of the structure of materials
  Using low energy (few MeV) TBA X-band gun

## Slide 34: XFEL in biar?
TBA---9GeV Compact FEL in BIAR regime
Fast filled accelerator
Yuliang Jiang, et al, PRAB 24, 112002 (2021)
Advantages:
Short pulses
Drive beam can generate RF at multiple frequencies
Automatically sync’ed
Challenges:
Still in research phase
Kickers
Waveguides

## Slide 35: WHY AAC? … Why SWFA?
AAC technology is versatile
Long-term
  1-10 TeV e+e- linear collider
  Higg’s Factory
Mid-term
  XFEL light sources
  Inverse Compton sources
Near-term
  Compact accelerators for societal applications or Stewardship (E.g. Industrial, Security, Medical applications.)
AAC Roadmap: PWFA, LWFA, SWFA
SWFA
  Positron acceleration
  Takes advantage of much existing technology from today’s accelerators
  Recent progress (few MV/m  300 MV/m at X-band, exploring GV/m …)
IP
e-
e+
3TeV
1
10
1
10
SWFA 3 TeV linear collider
SWFA XFEL

## Slide 36: Structure Wakefield Acceleration (SFWA)
Collinear Wakefield Acceleration
Accelerator Module
0.5 m
0.22 m
Main focus:
High Transformer Ratio
THz structure
Main challenges:
Temporal shaped high charge bunch
Beam Break up instability
Precise structure fabrication
corrugated metallic waveguide

## Slide 37: Electron beam-driven structure wakefield acceleration (SWFA)
Two Beam Acceleration (TBA)
Sicking, E., Ström, R. From precision physics to the energy frontier with the Compact Linear Collider. Nat. Phys. 16, 386–392 (2020).
https://doi.org/10.1038/s41567-020-0834-8
drive beam
main beam
CLIC
Quartz tube
AWA
PETS
Main focus:
High charge bunch trains
GHz structure
Main challenges:
Broadband RF couplers
Breakdown & efficiency
Cost of maintaining two beamlines
drive beam
main beam
Power Extraction and Transfer Structure (PETS)
Accelerator