## Slide 1
Development of FEL code to simulate the integrated undulator line
MyungHoon Cho
2024-11-14
1/21

## Slide 2
Contents
Introduction to FELIS code.
Bench mark
Future development
Summary

## Slide 3
- FEL is a radiation amplification by response of electrons and self-generated radiations.
Free-Electron Laser (FEL)
Electron beam current
Energy spread
Norm. emittance
Undulator field profile
FEL intensity
FEL pulse duration
- High gain FEL needs high beam current and well-defined undulator setting as well as very good electron beam quality.
microbunching
field amplification

## Slide 4
Free-Electron Laser (FEL)
Linac
Undulator (HX)
Exp.Hall (HX)
Exp.Hall (SX)
Undulator (SX)
Injector
PLS-II
PAL-XFEL
Project Period: 2011 ~ 2015
11-GeV Electron Linac (Normal Conducting S-band, 60 Hz)
Total Length: 1.1 km
 | Hard X-ray | Soft X-ray
Photon energy | 2.0 ~ 20 keV (0.6 ~ 0.06 nm) | 250 ~ 1250 eV (5 ~ 1 nm)
Beam energy | 4 ~ 11 GeV | 3 GeV
Repetition rate | 60 Hz | 60 Hz
Band width of pink beam (ΔE/E) | ~ 0.4 % | ~ 0.5 %
Photon flux (pink beam) | > 1.0 x 1011 phs/pulse | > 1.0 x 1012 phs/pulse

## Slide 5
FEL codes
and others ….
Averaged code
Unaveraged code

## Slide 6
Most popular FEL code is the averaged algorithm (like GENESIS 1.3), since it is fast.
Averaged Code
One simulation step can be multiple undulator period ().
Physics is averaged while electrons travel .
 Even though physics is approximated, it covers most of FEL phenomena. Moreover, fast calculation.

## Slide 7
For realistic situation, users have to consider more information such as wakefields, tapering undulator, phase shifter, chicane, self-seeding, and so on.
FEL Code calculation sequence
undulator
quad
- Basic components are undulators and quadrupoles which should be calculated in FEL code.
field solver
for space charge, high harmonics
calculation of Quads and K
particle push
more information of initial condition
Additional calculation : phase shifter, chicane, self-seeding, etc
. . .

## Slide 8
FELIS is the FEL code for simulating PAL-XFEL performance.
FELIS : the Free-Electron-Laser simulation using Integrated Slices
…..
Und.
Und.
Und.
Und.
…..
…..
Und.
Und.
Und.
Und.
…..
# Genesis 1.3
# FELIS
Electrons can cross adjacent slices.
Current density can be changed.
Space charge and wakefield can be varied.
Electrons moves in periodic boundary.
Current density is fixed.
Space charge and wakefield are fixed.

## Slide 9
Requirement
: C language, MPI library, Gnu-Scientific Library (gsl), HDF5 library (output file)
Functions
- 1D and 3D mode.
- Fundamental equations follow GENESIS 1.3 thesis.
- Field solver : Alternating-direction implicit (ADI) method
- Particle mover : 4th order Runge-Kutta method
- Shotnoise : Fawley algorithm
- Wakefield : numerical impedance calculation method
- Space charge field : Poisson solver using Green function
- chicane
- phase shifter : phase jump method
- self-seeding : Bragg forward wakefield model
Fawley, PRST-AB 5 070701 (2002)
K. Bane, PRST-AB 18 034401 (2015)
J. Qiang, Comp. Phys. Comm. 203 122 (2016)
S. Reiche, Ph.D thesis (1999)
FELIS : the Free-Electron-Laser simulation using Integrated Slices
R. Lindberg, PRST-AB 15 050706 (2012)
FELIS includes diverse calculation modules of chicane, phase shifter, self-seeding, and so on inspired by SIMPLEX FEL code.
Github : https://github.com/scienter/fel.git

## Slide 10
FELIS : electron beam loading
[EBeam]
beam_energy=8543 // [MeV]
energy_spread=0.017558 // [%]
peak_current=3000 // [A]
norm_emittance_x=0.4 // [mm mrad]
norm_emittance_y=0.4 // [mm mrad]
beta_x=25.6 // [m]
beta_y=13 // [m]
alpha_x=1.0
alpha_y=1.0
beamlets_in_bucket=2000
number_in_beamlet=4
Znodes=2
Z0=-10e-6
Z1=10e-6
Initial particle distribution
current distribution
Zn0=1
Zn1=1
Znodes=15
Z0=-17e-6
Z1=-13.5e-6
Z2=-10.0e-6
Z3=-8e-6
…
z_n0=0
z_n1=0.3
z_n2=0.7
z_n3=0.835
…

## Slide 11
FELIS : Wakefield
[Wakefield]
activate = ON
shape = Flat
ac_dc = AC
radius = 4.5e-3 // [m]
conductivity = 3.03e7
ctau = 2.4e-6 // relexation_time * light velocity [m]
FELIS implies the longitudinal wakefield automatically.
wake function
wake field for hole bunch
FELIS

## Slide 12
FELIS : quads and matching
[Quad]
numbers=13
unit_start = -0.0325 // [m]
unit_end = 9.9675 // [m]
quad_start = -0.0325 // [m]
quad_end = 0.0325 // [m]
g = ?? // [T/m]
[Quad]
numbers=13
unit_start = 4.9675 // [m]
unit_end = 14.9675 // [m]
quad_start = 4.9675 // [m]
quad_end = 5.0325 // [m]
g = ?? // [T/m]
Basic beam optics gives matching condition for the quad value ‘g’ with given ‘’.

## Slide 13
FELIS : quads and matching
After matching
[Quad]
numbers=13
unit_start = -0.0325 // [m]
unit_end = 9.9675 // [m]
quad_start = -0.0325 // [m]
quad_end = 0.0325 // [m]
g = 40 // [T/m]
[Quad]
numbers=13
unit_start = 4.9675 // [m]
unit_end = 14.9675 // [m]
quad_start = 4.9675 // [m]
quad_end = 5.0325 // [m]
g = -40 // [T/m]
Before matching
FELIS will recommend ‘quad q’ value for matching.

## Slide 14
diamond crystal
FELIS : self-seeding
[Chicane]
chicane_ONOFF=ON
delay_time = 50 //[fs]
position_z = 51 //[m]
dipole_length = 0.4 //[m]
dipole_distance_1 = 1.4 //[m]
dipole_distance_2 = 1.4 //[m]
selfseed_ONOFF = ON
energy_range=80 // [eV]
shift_energy = -30 // [eV]
washing_bunch = OFF
crystal_thickness = 100 // [um]
crystal_type = Diamond_220
Theoretical wake
Simulated wake
Self-seeding calculation is in option.

## Slide 15
FELIS : phase shifter
Phase shifters are used for optimizing FEL intensity.
phase shifter
BPM
quadrupole
Self-seeding
sinusoidal fitting
saturation region
in-phase
out-phase

## Slide 16
FELIS : phase shifter
[Phase_shifter]
number = 10
start_position = 6 //[m]
interval_length = 6 //[m]
phase = 1.15 //[pi]
Setting phase shifter will shift each electrons’ phase location.
gain curves by setting different phase
two color FEL by setting suppression of FEL lasing
Scientific Reports 13 13786 (2023)
PRAB 23 090702 (2020)

## Slide 17
FELIS : bench mark
1D comparisons of MEDUSA, PERSEO, PROMETEO, and FELIS.
static
time dependent
Single flat undulator and loading seed pulse.
L.Giannessi, Nuclear Inst. Methods in Phys. Research, Sec. A: Accelerators, Spectrometers, Detectors and Associated Equipment 5 143 (2008)
FELIS
FELIS

## Slide 18
FELIS : bench mark
3D comparisons of GENESIS 1.3, SIMPLEX, and FELIS.
energy [J]
FELIS
FELIS
Undulator tapering

## Slide 19
Comparing with PAL-XFEL
FEL intensity and spectrum are similar with the measurement.
energy
time
Undulator tapering
experiment
simulation
average of 10 data

## Slide 20
Further development
Elliptically polarized mode will be developed for future installation of the AppleX undulator.
Equation of particle motion
: polarity parameter
When , linear
When , circular
formula in GENESIS 1.3
It recovers GENESIS 1.3
Developing the elliptical wave equation is on-going.
1D model of the elliptical wave equation NJP 18 062003 (2016)

## Slide 21
Summary
FELIS is the FEL code to simulate PAL-XFEL performance.
All particles are loaded at beginning, so shifting particles between adjacent slices is possible.
Inspired from GENESIS1.3 and SIMPLEX, FELIS supports diverse application modules by simply setting options.
Simulation results well describe measurements in PAL-XFEL.
Further development will be for an arbitrary elliptical polarization case.