## Slide 1: CAPhE Lab Meeting
K. M. Nam
Science and Technology, Pohang 37673, Korea
2024/08/07

## Slide 2: Index
Introducing Myself
Introduction - Basic Concept, Research Interest
What I’ve done
Research Plan

## Slide 3: Introducing Myself
Name | Ki Moon Nam | E-Mail | ngw5756756@postech.ac.kr
Birth | 1992-11-26 | Address | PAL-ISSC 402
Tel | 010-9660-6360 |  | 
About Myself
I am a graduate student in the Division of Advanced Nuclear Engineering, scheduled to receive my Ph.D. on August 9, 2024. From August 16, I will officially begin my postdoc at CAPhE in POSTECH, focusing on relativistic beam dynamics. I am interested in a variety of beam dynamics in storage rings.
During my early years, I didn't have any senior students, so I navigated my lab life alone. I am very pleased to greet and meet the various members of CAPhE. I hope to maintain good relationships and conduct excellent research together moving forward

## Slide 4: Career
Pohang University of Science and Technology (POSTECH), Department of Physics
B.S.
M.S.
Ph. D.
2012.3 ~ 2017. 2
Pohang University of Science and Technology (POSTECH), Division of Advanced Nuclear Engineering
Major in Theoretical Accelerator Physics and Industrial Accelerator Design
Thesis : A Simulation Study of a ERL based EUV-FEL for Lithography
Advisor : Prof Gunsu Yun and Dr. Yong Woon Parc
2017.3 ~ 2019. 2
Pohang University of Science and Technology (POSTECH), Division of Advanced Nuclear Engineering
Major in Theoretical Accelerator Physics and Beam Dynamics
Thesis : Revised Hamiltonian near Third-integer Resonance and its dynamics in Electron Storage Ring
Advisor : Prof Gunsu Yun and Dr. Yong Woon Parc
2019. 3 ~ 2024. 8
Future
2024. 8 ~
Postdoc at CAPhE, Postech.
Advisor : Prof. Moses Chung

## Slide 5
Introduction

## Slide 6: Storage Ring and Tune
A storage ring circulates electrons in a circular orbit using various magnets.
Electrons oscillate around this orbit as they circulate and the number of oscillations per turn is called the tune and denoted as .
Tune is mainly determined by the dipole and quadrupole; initial electron conditions do not affect tune.
In general, tune is set to avoid rational numbers.
Schematic layout of a storage ring
Dipole
Quadrupole
Motion of Stable Electron in a storage ring
3 cycle
4 cycle
0.4117 cycle
1 cycle
2 cycle
4 cycle
1 cycle
2 cycle
3 cycle
Sextupole
Notes: A storage ring circulates electrons in a circular orbit using various magnets.
Electrons oscillate around this orbit, and the number of oscillations per turn is called the tune.
In this figure, the electron oscillates one, two, three, four, and a little more, so the tune is 4.4117.
Generally, the tune is set to avoid rational numbers.

## Slide 7: Tune and Resonance
When external forces with position-dependent properties are present, they affect the system.
If the tune is an integer multiple of a resonance, these external forces accumulate continuously and it makes electrons diverge.
Schematic layout of a storage ring
Motion of Stable Electron in a storage ring
Dipole
Quadrupole
Sextupole
4 cycle
1 cycle
2 cycle
3 cycle
Third Integer Resonance
Notes: When external forces with position-dependent properties are present, they affect the system.
As shown in this figure, if the electron's tune is an integer, it experiences external forces every turn, eventually causing divergence.
If the tune's times 3 is integer, the electron experiences the same force every 3 turns.
If the sum of these forces over 3 turns is not zero, the electron diverges.

## Slide 8: Source of External Force
Stable
Stable
Ideal (No Electron Energy Deviation)
Nonlinear Phase Space Distortion Due to Sextupole magnet
Sextupole o
Helmut Wiedemann et al., Springer (4th edition), 2007
Practical (Chromatic effect and correction)
This distortion exerts an external force on electrons
Notes: Let me explain the source of these external forces.
Storage rings include sextupole magnets to correct chromatic effects.
However, sextupoles also cause some phase space distortion.
This distortion acts as the external force mentioned earlier.

## Slide 9: Phase Space (Near Resonance)
Loss
Loss
Loss
Resonant Islands
Boundary
Boundary
Third Integer Resonance
Boundary
Loss
Loss
Loss
Loss
By adjusting sextupole
)
Primary Orbit
Notes: When the tune's integer multiple is close to a rational number, sextupoles distort the phase space as shown.
In the stable primary orbit region (sum of F_external = 0), the electron remains stable.In other regions, the electron diverges unless sextupoles are adjusted to make the sum of F_external zero in specific phase space regions.
This adjustment creates resonant islands, which are stable and spatially separated from the primary orbit.

## Slide 10: Research Interest
Theory of Resonant Islands, Amplitude-Dependent Tune Shift, Phase-Dependent Tune Shift and Devil’s Staircase
Application : Bunch Separation, Extraction, Etc.
M. Giovannozzi et al., PRL (2002)
Markus Ries et al., Synchrotron SOLEIL 2016
4th order Splitting (SPS)
9000 turn
0 turn
42000 turn
34000 turn
Separation for Multi Mode Operation (BESSY II)
3rd order Splitting (SPS)
2000 turn
0 turn
20000 turn
4000 turn
R. Cappi et al., PRST-AB (2004)
Nonlinear Dynamics
(Ex. Distortion)
Resonant Dynamics
(Ex. Divergence)
Notes: Several accelerator facilities have utilized this property.
BESSY II successfully separated bunches into resonant islands to create multiple photon beams.SPEAR3 also conducted similar bunch storage experiments.
At CERN, this method is used to split electron beams into resonant islands by reducing the boundary size of the primary orbit.Despite these experimental successes, theoretical support is still lacking.

## Slide 11
What I’ve done

## Slide 12: Result (New Parameter)
shows bad match, so I suggested the revised one.
Contours with shows better performance than those of .
KM Nam et al., PRAB (2024)
(b)
(a)
KM Nam et al., PRAB (2024)
Theory
Tracking
Theory
Tracking

## Slide 13: Result (New Parameter, Varying tune)
While varying tune, contours with shows better performance than those of.
KM Nam et al., PRAB (2024)
Theory
Tracking
Theory
Tracking

## Slide 14: Phase Space Manipulation
Developing a 50 MeV LPA-based Injector at ATHENA for a Compact Storage Ring (unpublished)
Previously, phase space was predicted from lattice information.
This approach outlines constructing lattices to achieve desired phase spaces.
Dipole
Quadrupole
Sextupole

## Slide 15: Phase Space Manipulation
?
Previously, phase space was predicted from lattice information.
This approach outlines constructing lattices to achieve desired phase spaces.
Developing a 50 MeV LPA-based Injector at ATHENA for a Compact Storage Ring (unpublished)
Dipole
Quadrupole
Sextupole

## Slide 16: Phase Space Manipulation
!
Previously, phase space was predicted from lattice information.
This approach outlines constructing lattices to achieve desired phase spaces.
Chromaticity should be also considered simultaneously
Developing a 50 MeV LPA-based Injector at ATHENA for a Compact Storage Ring (unpublished)
Dipole
Quadrupole
Sextupole
but

## Slide 17: Phase Space Manipulation
Dipole
Quadrupole
Sextupole
!
Previously, phase space was predicted from lattice information.
This approach outlines constructing lattices to achieve desired phase spaces.
Chromaticity should be also considered simultaneously
Developing a 50 MeV LPA-based Injector at ATHENA for a Compact Storage Ring (unpublished)
but

## Slide 18
Research Plan (Future Paper)

## Slide 19: Outline
Conventional Hamiltonian cannot predict the motion of electron confined in closed region.
In conventional models, the action should not change.
If the action is the same, do particles with the same action have the same tune?
Devil’s Staircase phenomenon -> Need for theoretical calculations on dynamics.
Devil’s Staircase (flat tune region)
Nonlinear Filamentation
0.335
0.334
0.333
0.332
Filamentation
Nonlinear Filamentation

## Slide 20: Outline
Conventional Hamiltonian cannot predict the motion of electron confined in closed region.
In conventional models, the action should not change.
If the action is the same, do particles with the same action have the same tune?
Devil’s Staircase phenomenon -> Need for theoretical calculations on dynamics.
Devil’s Staircase (flat tune region)
Nonlinear Filamentation
0.335
0.334
0.333
0.332
Filamentation
Nonlinear Filamentation

## Slide 21: Outline
Conventional Hamiltonian cannot predict the motion of electron confined in closed region.
In conventional models, the action should not change.
If the action is the same, do particles with the same action have the same tune?
Devil’s Staircase phenomenon -> Need for theoretical calculations on dynamics.
Devil’s Staircase (flat tune region)
Predicted Result
0.335
0.334
0.333
0.332
Predicted Result
Nonlinear Filamentation

## Slide 22: Vs Tracking Data
Blue dots are tracking results and orange line is theoretical prediction
In the primary orbit, increases indefinitely with each turn. Therefore, as the averaging range increases, the average value converges to a constant. In contrast, in the islands, is confined, so as the averaging range increases, the average value of converges to zero.
Islands
Primary Orbit
Devil’s Staircase

## Slide 23
Thanks you

## Slide 24: Contour (Lie transform)
(a-c) : Weak high order effect (sextupole) Family
(d-f) : Strong High Order Effect Family
The larger the high order effect, the better the effect of using Lie perturbation..

## Slide 25: Lie Transform (APPENDIX행)
Consider the Generating function
When we consider ,
Consider the two successive Canonical transform. If , we can transform
Lie Transform
Mello

## Slide 26: APPENDIX로 날리자
Second Order Better Matching
정량화 정의도 써야 함

## Slide 27: Lie Transform (Result)
Variable transform coefficients are in Thesis
Lie Transform
Mello

## Slide 28: Dynamics in Islands
For
, and
, and