## Slide 1: Research Plan
Jan. 03. 2025
송우진

## Slide 2
Time table
1. Photon beam profile monitor (ionization profile monitor)
25.01
4GSR 장비 심의 및 발주.
Internal review meeting for 장비 심의 on Jan. 8th.
PAL-XFEL XIBPM upgrade and test at SX beamline
25.02
Equipment fabrication
Complete the draft of the design paper or include the content of the XFEL experiment.
25.05
Chamber fabrication will take 2–3 months, while there are no deadline issues for other components.
Complete fabrication
Vacuum test
PLS-II BL-6C test

## Slide 3
Time table
1. Photon beam profile monitor (ionization profile monitor)
XIBPM upgrade test plan
Jan. 06. – XIBPM upgrade, replacement of internal structures.
Jan. 08. – Discuss plans for measuring profile.
Jan. 13. – Vertical displacement measurement @ pink-beam
Jan. 14-17. – Chamber rotation and flange re-assemble
Jan. 20. – Horizontal displacement measurement @ pink- & mono-beam
(Plan) After Horizontal Experiment
Target – Profile measurement test, Calibration method validation.
Method – Extremely high magnification to measure profile (XFEL beam size is ~50 um, current design resolution ~ 100 um)
 Measurable range simulation in progress (to be discussed on 8th)

## Slide 4
PAL-XFEL photon beam profile measurement
Rep <-> E2 Diff. ↑-> large gradient
MCP V↑ -> gradient ↑
Magnification = x2.90
E2
E1
Shield
Repeller

## Slide 5
Time table
2. Cherenkov diffraction radiation based (electron) beam diagnostics
Background
Beam profile monitor
Beam position monitor
Classical Cherenkov radiation
Polarization, Diffraction
Beam profile (size)
Form factor, Coherence
Bunch length (sub-pico)
Impact parameter
Beam position
Radiation spectrum
Coherent THz source
Emission angle
Bunch length
THz Source
R/O electronics
Camera, Optics
Photodiode
BPM electronics
Spectrometer
Conceptual Design

## Slide 6
Time table
2. Cherenkov diffraction radiation based (electron) beam diagnostics
Before installation
Radiator design and manufacture
Set-up
Data acquisition system
Alignment test
Future plan
Installation
Alignment at e-Labs
Experiment
Radiator fabrication
Securing test facilities
Calculation of the target range
Detector (Spectrometer or power meter)
Experiment (1st test at IBS)
Beam profile monitor
Bunch length measurement

## Slide 7
GUN-I Section
(200 pC, 6 MeV, 10 Hz)
GUN-II Section
(200 pC, 70 MeV, 10 Hz)
GUN-I
GUN-II
S1
S2
S3
ICT
BAM
ACC
BPM test stand
UED exp.
Optical table
diagnostics
Advanced compact accelerator exp.
Configuration of e-Labs

## Slide 8
Radiator design
Accumulation
Al Coating

## Slide 9
Set-up
7-axis stage
1축 linear motor (Impact factor)
1축 manual (Hight)
5축 motor (Alignment)
Electron beam
ChDR

## Slide 10
Set-up
Electron beam
ChDR

## Slide 11
Data acquisition system
Control PC
Main PC
Control room
Gallery
LAN hub
5-axis controller
1-axis controller
1-axis motor
5축 controller
Camera
Camera
Tunnel (Optical table)
Chamber
5-axis motor
USB, Serial
LAN
20m USB extension
Chamber
Tunnel (Optical table)
Gallery (PC)

## Slide 12
Data acquisition system
1-axis motor controller
5-axis motor controller
Camera 1 (ChDR)
Camera 2 (YAG)

## Slide 13
Alignment test
DAQ test

## Slide 14
Alignment test
Laser
(e-beam)
SCM2
SCM1
Cor1
Cor2
Radiator
YAG
Camera
+lens f~30mm
9.53 mm
12.47 mm
Laser
(ChDR)
Camera
Positioning the camera to fit the ChDR total reflection path
Adjust the position to cover two views with one camera
Alignment based on initial beam path (SCM1-2)

## Slide 15
Alignment test
Laser
(e-beam)
SCM2
SCM1
Cor1
Cor2
Radiator
YAG
Camera
+lens f~30mm
9.53 mm
12.47 mm
Laser
(ChDR)
Camera
Positioning the camera to fit the ChDR total reflection path
Adjust the position to cover two views with one camera
Alignment based on initial beam path (SCM1-2)

## Slide 16
Alignment test
Laser
(e-beam)
SCM2
SCM1
Cor1
Cor2
Camera
Camera
+lens
12.47 mm
Laser
(ChDR)
Lens
MVL35M23 (35mm)
MVL7000 (Zoom 18-108)

## Slide 17
Horizontal profile
Vertical profile
Expected results
3 GeV 600 nm 0’

## Slide 18
100 MeV 600 nm 20’

## Slide 19
Bunch length measurement
What we Measure
(Coherent ChDR)
What we already know
(Incoherent / Single particle ChDR)
What we want to know
(Bunch length)
IBS 150 TW Laser, LWFA experiment
Expected e-beam parameters: 500 MeV, 1~5 fs(0.3~1.5 um), 10 pc

## Slide 20
Radiator (with capillary) design
Spectrometer

## Slide 21
Experimental set-up
Laser
Capillary
Au Mirror
Au Mirror
ChDR
ChDR
ChDR
ChDR
Window
LWFA Experiment with IBS 150 TW Laser
The goal was to measure the length of the electron beam. (500 MeV, a few fs, 10 pC)
Measuring ChDR coming off the edge of a capillary.
Beam transported using a 3’ Au mirror.
Outside the chamber, only passes through the filter and directly into the detector.
ChDR
Window
THz filter
Detector
Capillary
ChDR
Filtered signal

## Slide 22
Experimental set-up
THz filter
THz detector (power meter, 0.1~30 THz)
Measurement Target: Regions where the trends of Incoherent ChDR and Coherent ChDR differ.
  As the bunch length increases, differences appear at lower frequencies.(1 fs  ~80 THz, 5 fs  ~ 20 THz)
Measurement Plan: Use filters up to 20 THz and replace 5 filters sequentially from the highest frequency.
  Record beam energy and, if possible, beam size for each measurement.

## Slide 23
Conclusion
Electron Beam Profile Monitor
The current profile monitor is disassembled for cleaning.
Reassembly is planned in the tunnel before the scheduled installation at e-Labs.
After e-Labs installation:
  Perform laser-based alignment (2-axis).
  Follow with beam-based alignment (5-axis).
Significant time is expected to be required for alignment before actual ChDR measurements.
Bunch Length Measurement
The first experiment using the IBS 150 TW laser failed.
Aiming to find a facility capable of sub-pico bunch length experiments and reattempt using the same method.

## Slide 24: Appendix - Theoretical Background on ChDR

## Slide 25: Cherenkov Radiation
- Cherenkov(or Vavilov-Cherenkov) radiation is electromagnetic radiation emitted when charged particle moves faster than the light.
- The radiation is named after the Soviet scientist Pavel Cherenkov who was the first to detect it experimentally under the supervision of Sergey Vavilov at the Lebedev Institute in 1934.
- A theory of this effect was developed in 1938 within the framework of Einstein’s special relativity theory by Igor Tamm and Ilya Frank.

## Slide 26: Classical Cherenkov Radiation
Particle speed :
Light speed (in medium) :
Emission angle :
Vacuum
Glass
Beam

## Slide 27: Classical Cherenkov Radiation
Charged particle moving with constant velocity and the charge and current densities
Power spectrum at
T(avg time=1/2*(t+t’))
: no radiation
Frank-Tamm formula (1937)
: EM radiation emitted

## Slide 28: Classical Cherenkov Radiation
ε=2  Cherenkov angle θ = 45°
The number of photons emitted
per unit length per solid angle
Cherenkov angle θ

## Slide 29: Polarization radiation

## Slide 30: Cherenkov Diffraction Radiation
The radiation field is a solution to the vacuum macroscopic Maxwell equation with the polarization current.
Maxwell’s equations lead to the following equation for the magnetic field of polarization radiation:
The spectral-angular density of polarized radiation can be determined from the relation
Substance

## Slide 31: Cherenkov Diffraction Radiation
: Vertex angle of the prism
: Azimuthal angle
: Polar angle
: Impact parameter : Wavelength

## Slide 32: Cherenkov Diffraction Radiation
Intensity of ChDR vs h and λ
Intensity of ChDR vs h and λ

## Slide 33: Beam profile monitor
Extremely small divergence of ChDR
y
z
~mrad
Radiator