## Slide 1: Progress of deflecting cavity and status of eLABs
25. 01. 10
Geunwoo Kim

## Slide 2: Outline
Current Status of eLABS Facility
Transverse deflecting cavity design study
CST and ASTRA Simulation
Next Steps

## Slide 3: Current status of elabs facility.
3
Previous: RF was turned on, and Dr. Min worked on the laser setup.
Current: Due to ongoing repairs, progress is delayed. Tests will proceed whenever time allows.
Operation Plan: : If all systems stabilize, more tests may be possible during the XFEL maintenance in Feb.
+) Deflecting cavity manufacturing status: Disk, cylinder, coupler

## Slide 4: Review
4
RF
deflecting
cavity
E0
Beam
x’
Computer
(Data processing)
Screen
Brief concepts of Transverse Deflecting Cavity (TDC)
① Design and tunning
② Theory
Force
Force

## Slide 5: Primarily priority for design TDC
Power efficiency
  High r⊥ ()
  High Quality factor Q
  Low group velocity vg
Manufacturing costs
  Not to challenge for its manufacture
5
Force
Force
RF system
(Power generation)
Transmission
Deflecting cavity
Load
<Simple flowchart of TDC>
RF Input
RF Output
Field formation
z
y

## Slide 6: Designed TDC feature
Main feature of elabs TDC
HEM11 field mode (TE11 + TM11 mode)
  Can get high deflecting voltage VT.
  Higher r⊥ compared to TM11 mode.
Disk-loaded structure (a.k.a slow-wave structure)
  Need to suppress less than by disk.
  2π/3 operation mode (ΔΦ = 2π for 3 cells) operation
  Higher r⊥ than the other mode.
Travelling-wave and mode suppressors.
2/3π mode operation
6
<E-field distribution>
z
y
Coupler cell
Active cells
Coupler cell
Power
efficiency
Manufacturing costs

## Slide 7: Designed TDC feature
1. Hybrid electro-magnetic mode (HEM11)
  Composed of transverse electromagnetic modes.
    TE compose each iris section.
    TM compose each the middle of cell.
   -Ey and Hx  -Fy
  : Both E and H field kick the beam
   High r⊥, high V ⊥  High power efficiency.
7
2/3π operation mode
ΔΦ = 4π
<E-field distribution>
z
y
Beam
Beam
<H-field distribution>

## Slide 8: Designed TDC feature
2. Disk-loaded structure
Why we choose disk-loaded structure?
  First, in uniform cavity
  Slow-wave structure is needed.
  Some structure have higher r⊥, but too high vg or hard to manufacture.
8

## Slide 9: Designed TDC feature
Why 2π/3 mode operation was selected? (Efficiency of the structure)
  Fewer disks required than π/2 mode.
    Not only cheaper manufacturing cost but also higher r⊥ .
  Quality factor Q =
  Thick disk → low vg → Enhanced power efficiency.
9
RF system
(Power generation)
Transmission
Deflecting cavity
Load

## Slide 10: Designed TDC feature
3. Travelling-wave and mode suppressors.
Standing vs Travelling wave
  In standing wave, only half power assist deflection components.
  Need a few μm waiting time to develop fields in cavity.
     May damage RF system.
  In opposite case, all the above problems are not a concern.
10
<Principal of standing and travelling wave>
RF system
(Power generation)
Transmission
Deflecting cavity
RF system
(Power generation)
Transmission
Deflecting cavity
Load

## Slide 11: Designed TDC feature
3. Travelling-wave and mode suppressors.
Backward travelling wave
  High Quality factor Q (Low field loss).
  Easy to contorl phase variation.
11
<Backward travelling-wave example>
vg
vp
<Simple flowchart of TDC>
RF Input
RF Output
Field formation
z
y
Beam

## Slide 12: Designed TDC feature
Mode suppressors (Mode isolators)
  Damping unwanted operation mode like HOM dampers in RF cavity.
12
Mode suppressors
2π/3 mode @ 2.85603 GHz
2π/9 mode @ 2.849 GHz
7π/9 mode @ 2.86725 GHz
2π/3 mode @ 2.88247 GHz
Maybe due to B.C.

## Slide 13: CST simulation of TDC
Single cell
  for cylindrical waveguide.
13
2b
c
p
2a
t/2
d
Variables | Mean Δf/Δs [MHz/mm] | STD [MHz/mm]
sb | -2.665 | 0.080
sa | -0.386 | 0.002
smode | -0.048 | 0.005
sd | 0.039 | 0.014
sc | 0.095 | 0.012
st | 0.025 | 0.003
Dispersion relation

## Slide 14: Analysis of TDC
Coupler cell
  Reflection coefficient
  VSWR (Reflection value) < 1.05 or 1.1
   Next, field flatness study…
14
wc
Lc
rc
RF system
(Power generation)
Transmission
Deflecting cavity
Load
~1.02
~1.02
Variable in Kyhl’s tuning

## Slide 15: ASTRA simulation status
15
V⊥ | Slope | offset
0.5 MV | -0.226 | -6.70
2.0 MV | -0.917 | -26.92
ΦTCAV | Slope | offset
90 deg | -0.226 | -6.70
-90 deg | 0.227 | 6.70
In an ideal situation, no offset exists.

## Slide 16: Summary
TDC design study done.
CST and ASTRA simulation conducted.
Next steps
  elabs: under maintenance
  Field flatness optimization pending (CST)
  ASTRA phase matching
16

## Slide 17: Appendix A
Without damper
17
2π/9 mode @ 2.86491 GHz
π/9 mode @ 2.86153 GHz
2π/3 mode @ 2.8713 GHz
7π/9 mode @ 2.88164 GHz
Mode damper
π/9 mode @ 2.84522 GHz
2π/9 mode @ 2.849 GHz
2π/3 mode @ 2.85603 GHz
7π/9 mode @ 2.86725 GHz
Mode damper 90deg rotated
8π/9 mode @ 2.88353 GHz
π/9 mode @ 2.87225 GHz
2π/9 mode @ 2.87585 GHz
2π/3 mode @ 2.88247 GHz

## Slide 18: Appendix B