## Slide 1: Active Harmonic Cavity Analysis
Young Min Park
Division of Advanced Nuclear Engineering (DANE), POSTECH
2025-01-17, Pohang, South Korea

## Slide 2: Index
Previous work
Active harmonic cavity
  Overview
  Without beam loading
  With beam loading
4GSR analysis
  Main cavity
  HHC
Simulation result
Conclusion
2

## Slide 3: Previous work
3/23
Bunch lengthening
N
S
Undulator
Main cavity
Beam loses energy due to bending or insertion devices, and the lost energy is replenished through the RF cavity.
Flattening the voltage slope at the energy replenishment location can increase the bunch length.
The well-known method for flattening the voltage slope is using a Higher Harmonic Cavity with the harmonics of the Main cavity.
Previous work focused only on bunch lengthening using passive cavities, but since the 4GSR uses active cavities for bunch lengthening, a study on the physics of active cavities was conducted.
Radiation loss

## Slide 4: Active Harmonic Cavity
4/23
Power generator
Waveguide
Coupler&Cavity
Modulator
Klystron
Waveguide
Waveguide
Cryostat
Overview
Active cavity
Passive cavity

## Slide 5: Active Harmonic Cavity
5/23
Without Beam Loading
We can consider a simplified circuit.
Ignore beam loading effects, only focus on generator-cavity coupling.
describes the coupling between the generator and the circuit.
Impedance of cavity
Real axis is in-phase voltage seen by beam.

## Slide 6: Active Harmonic Cavity
6/23
With Beam Loading
Considering beam loading effects.
Beam current causes a voltage in the transmission line, and this leads to a backward(reflected) wave.
Voltage and phase of cavity is determined by .
Optimum and to minimized can be calculated by below equation.

## Slide 7: 4GSR bunch lengthening
7
Ring parameter
This is not an exact flat potential condition (NFP).
This setup allows for operation without using an HHC and modifying the main cavity.

## Slide 8: 4GSR main cavity
8
Parameter | Values | 
Frequency [MHz] | 500 | 
Max. power coupler [kW] | 120 | 
Unloaded quality factor | 29909 | 
R/Q [] | 113.68 | 
Coupling factor | 1 ~ 5 | 
Parameter | Values | 
Frequency [MHz] | 500 | 
Max. power coupler [kW] | 120 | 
Unloaded quality factor | 29909 | 
 | 113.68 | 
Coupling factor | 1 ~ 5 | 
Ring parameter
Cavity parameter
Reduce number of cavity per cavity increases Reduced installation space, low installation costs
BESSY-II/ EU-HOM damped cavity

## Slide 9: 4GSR harmonic cavity
9
Parameter | Values | 
Frequency [MHz] | 1500 | 
Max. power [kW] | 20 | 
Unloaded quality factor | 14000 | 
R/Q [] | 86 | 
Coupling factor | 1 ~ 3 | 
Parameter | Values | 
Frequency [MHz] | 1500 | 
Max. power [kW] | 20 | 
Unloaded quality factor | 14000 | 
 | 86 | 
Coupling factor | 1 ~ 3 | 
Ring parameter
Cavity parameter
ALBA 3rd Harmonic cavity

## Slide 10: Simulation result
10
Ring parameter
By using pyAT(python Accelerator Toolbox) Setting : 1 Bunch, 50000 Macroparticles
Can achieve a 4 times increase in bunch lengthening.
However, Severe instability observed when wake is included, deviating from analytical results.
Simulations conducted with only the main cavity for further investigation.
W/o Wake
HHC off
HHC on

## Slide 11: Simulation result
11
Ring parameter
Problems
w/o HHC, Wake on,
?
Centroid Shift
Suspected that beam loss occurred due to the centroid shift crossing the bucket separatrix.
Need to investigate the cause of the centroid shift observed in the simulation.
Head-tail? Robinson?
Beam loss occurs
In the example file of ESRF, the centroid shift is also observed.
High single bunch current suspected as the cause.

## Slide 12: Simulation result
12
Ring parameter
Multi-bunch Simulation
w/o HHC, Wake on, , 1332 Bunches(1332 Macroparticles)
?
Centroid Shift
Observed a centroid shift of a similar scale to the single bunch case.
The calculated damping time is 9.4 ms, while the fitted value is 11.2 ms.
Signs of instability in other modes are observed, suggesting that analysis using STFT would provide more accurate insights.
The presence of two modes might be due to a multi-bunch instability with .
The cause of the centroid shift remains unclear and requires further investigation.

## Slide 13: Conclusion
Conducted a study on the conditions for steady state operation with an active cavity.
Identified the conditions for both the 4GSR main cavity and the HHC cavity.
Performed tracking simulations using pyAT and compared the results with analytical predictions
Problems
  A beam loss occurred at the location where Robinson instability does not take place due to centroid shift.
Research plan:
  Insert Harmonic cavities and wake fields and reran the simulation.
  Remove 300 bunch to makes gaps and observe transient effects.
  Optimized parameters of the main cavity and HHC cavity according to the Robinson instability analysis.
13/23

## Slide 14: Thank you for your attention!
14/23