## Slide 1: Research Progress
Feb. 14. 2025
송우진

## Slide 2
Expected signal strength
  4 – Exposure time estimation
Transverse spread
Systematic error
Summary of White PBPM Development
3. Detailed Design
5. Resolution (Dec 06, 24)
4. Experiment
1. Background Study
2. Conceptual Design
Experimental plan (Nov 01, 24 )
  Experimental goal and contents
  Preliminary preparations
  Detailed experimental procedure
Set-up
  1 – 장비심의위원회 (Feb 05, 25)
  2 – Order
  Fabrication
Test
  XFEL SX test plan (Jan 03, 25)
  3 – PAL-XFEL Soft X-ray beamline
    Data processing
    Data analysis
    Results (in progress)
  PLS-II BL6C

## Slide 3
Time table
Jan 06 – XIBPM upgrade, replacement of internal structures.
Jan 08 – Discuss plans for measuring profile.
Jan 13 – Vertical displacement measurement @ pink-beam
– Chamber rotation and flange re-assemble
Jan 20 – Horizontal displacement measurement @ pink- & mono-beam
Feb 05 – 4GSR 가속기연구단 장비검토위원회
Feb 10 – Start of major component procurement
(Plan)
March – Profile measurement at PAL-XFEL SX beamline (Replace mesh and electrode with an upgraded version)
April – Complete the draft of the paper works (Thesis, Journal)
May – Experimental chamber set-up and test

## Slide 4
장비심의위원회

## Slide 5
Procurement item list

## Slide 6
PAL-XFEL Soft X-ray beamline experiment overview
From H. Hyun’s presentation
X-ray

## Slide 7
PAL-XFEL Soft X-ray beamline experiment overview
Jan 06 – XIBPM upgrade, replacement of internal structures.
Jan 08 – Discuss plans for measuring profile.
Jan 13 – Vertical displacement measurement @ pink-beam
– Chamber rotation and flange re-assemble
Jan 20 – Horizontal displacement measurement @ pink- & mono-beam
 In this experiment, Keep the mesh, only Install the shield plate.

## Slide 8
PAL-XFEL Soft X-ray beamline experiment overview
Grating mirror
XIBPM
Pop-in Monitor (PM)
YAG  Reference
19.04 m
14.58 m
Image ration: 1.766

## Slide 9
PAL-XFEL Soft X-ray beamline experiment overview
Experimental target
Vertical / Horizontal displacement
   Beam path change
Point spread function (Beam size)
  Applied voltage change
  Photon beam energy change, Pink / Mono beam
1. Repller, electrode size
 About 4% increased
2. Shield plate position
 About 4% increased
By applying the same voltage to Mesh 1 as MCP-in, it is possible to mitigate the magnification increase (M=1.04).
Set A
Set B

## Slide 10
PAL-XFEL Soft X-ray beamline experiment results (Vertical, in progress)
1. Data processing
500 eV, position 0, shot 1
Center position and size of each column

## Slide 11
PAL-XFEL Soft X-ray beamline experiment results (Vertical, in progress)
1. Data processing
Center shifted image

## Slide 12
PAL-XFEL Soft X-ray beamline experiment results (Vertical, in progress)
2. Data analysis (Voltage set A/B)
Set A
Set B

## Slide 13
PAL-XFEL Soft X-ray beamline experiment results (Vertical, in progress)
2. Data analysis (Photon energy)
500 eV
700 eV
900 eV
1100 eV
Kr binding energy  M (293 eV), L (1678 eV)

## Slide 14
PAL-XFEL Soft X-ray beamline experiment results (Vertical, in progress)
2. Data analysis (Photon energy)
500 eV
700 eV
900 eV
1100 eV

## Slide 15
PAL-XFEL Soft X-ray beamline experiment results (Vertical, in progress)
2. Data analysis (Position) - M4 Mirror’s GR motor adjusted (8 steps)
Pop-in Monitor
XIBPM displacement
= 1.027
PM displacement
= 1.87
(1.87/1.766=1.059)

## Slide 16
PAL-XFEL Soft X-ray beamline experiment results (Vertical, in progress)
2. Data analysis (Position) - M4 Mirror’s GR motor adjusted (8 steps)
Grating mirror
XIBPM
Pop-in Monitor (PM)
YAG  Reference
19.04 m
14.58 m
Image ration: 1.766
Set A
Fit err = 8.9e-3, 7.2e-2
Set B
Fit err = 1.76e-2, 1.44e-1

## Slide 17
PAL-XFEL Soft X-ray beamline experiment results (Vertical, in progress)
2. Data analysis (Applied voltage)
-1400 V
-1600 V
MCP-in voltage
Repeller
voltage
2000 V
3000 V
4000 V

## Slide 18
Exposure time estimation
Measured by XIBPM at SX beamline (Kr injected)
900 eV pink beam single shot, SNR~4
PAL-XFEL SX beamline, photons per pulse  2e+12 (pink beam)*
Xenon ionization cross section at 900 eV (Kr was used, but since the cross-section is similar, Xe data will be utilized for a consistent comparison.)  2.1 Mbarn
Photo-ion generation (event number) per pulse  2.24e+5 [event/pulse]
* S. H. Park, RSI 89, 055105 (2018)

## Slide 19
Exposure time estimation
Pressure = 1e-6 torr
# of event = Photon flux * Cross-section (Xe) * Loschmidt constant * Pressure * Drift length [event/s/0.1% B.W.]
Photon beam | Beamline | Total event number | Exposure time
900 eV pink beam | PAL-XFEL SX | 2.24e+5 | Single pulse
White beam | PLS-II | 3e+9 | Dep. on data processing time
 | 4GSR | 8e+9 | 
10 keV beam (0.1% bW) | PLS-II | 1.85e+5 | 1.21 sec (0.83 Hz)
 | 4GSR | 2.50e+6 | 0.09 sec (11 Hz)
30 keV beam (0.1% bW) | PLS-II | 5.09e+2 | 440 sec
 | 4GSR | 2.59e+4 | 8.7 sec (0.12 Hz)

## Slide 20
Exposure time estimation
Gas | Percentage contribution
H2O | 48%
H2 | 27
N2 | 15
O2 | 5
CO | 2.5
CO2 | 2.5
Total | 100%
Photon beam | Beamline | Total event number |  | Exposure time (Residual gas)
 |  | Xenon | Residual Gas | 
900 eV pink beam | PAL-XFEL SX | 2.24e+5 (Kr) |  | Single pulse
White beam | PLS-II | 3e+9 | 9.2e+7 | 2.4 ms (410 Hz)
 | 4GSR | 8e+9 | 1.76e+8 | 1.2 ms (785 Hz)
10 keV beam (0.1% bW) | PLS-II | 1.85e+5 | 6.07e+2 | Too long
 | 4GSR | 2.50e+6 | 8.19e+3 | 274 sec
30 keV beam (0.1% bW) | PLS-II | 5.09e+2 | 1.03e+0 | Too long
 | 4GSR | 2.59e+4 | 5.24e+1 | Too long
Residual gas composition (High vacuum, require reference check)

## Slide 21
Future plan
Spectra → BL6C Beam Calculation (Previously Calculated with IVU20)
Simulate the expected experimental results for BL6C, including the event number.

## Slide 22
Summary
White PBPM is currently in the procurement process.
XIBPM displacement experiment at the PAL-XFEL SX beamline has been completed.
- Data analysis is in progress.
Expected signal intensity has been calculated.
- Simulation for the PLS-II experiment is planned.

## Slide 23
500 eV
700 eV
900 eV
1100 eV

## Slide 26
H2
H2O
N2, O2
CO2?
진공도 : 6.9E-7 Torr
250113_XIBPM - RGA 측정