## Slide 1
20250310 Group Meeting
20250310 Group Meeting
10, Mar 2025
Minseo Jeong

## Slide 2
2
20250310 Group Meeting
Outline
Experimental Progress
Source Code for Optimization of UED Machine Parameters
- Multi-objective Bayesian Optimization

## Slide 3
Experiment Progress
20250310 Group Meeting
3
Measurement of emittance by CCD camera(C9100-13) and quadrupole
Parameter | Value
Quadrupole length | 0.090m
Drift | 2.325m
Σsem=MΣquadMT (Σ= where σ11=εβ, σ22 =εγ, σ12= σ21= -εα, M=)

## Slide 4
Experiment Progress
20250310 Group Meeting
4

## Slide 5
Multi-objective Bayesian Optimization
20250310 Group Meeting
5
Notes: HV: size of the portion of the objective space that is dominated by the PF
IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 6
Multi-objective Bayesian Optimization
20250310 Group Meeting
6
Gaussian process(GP): the surrogate model which represents function value at random input variable via multivariate Gaussian distribution
- f(x) ∼ GP[μ(x), k(x,x’)]
Kernel(k(x,x’)): a function which represents covariance between two input points
-
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 7
Multi-objective Bayesian Optimization
20250310 Group Meeting
7
Commonly used kernel:
-Radial basis function()
-Matern function: generalized version of RBF kernel
is modified Bessel function of second kind,
ν=3/2 or 5/2)
Length scale hyperparameter l should be optimized by maximizing marginal log-likelihood(MLL)
- log p(y|X, θ)= −yTK-1 yy/2-log |Ky| −n/2 log 2π
R. Roussel et al. Phys. Rev. Accel. Beams 27. (2024).
Notes: θ is the set of GP model hyperparameters
The first term is the data fit term which is maximized when model predictions accurately predict experimental data.
The second term describes model complexity and is maximized given the simplest model,
The final term is a normalization constant based on the number of training points in the dataset.
IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 8
Multi-objective Bayesian Optimization
20250310 Group Meeting
8
Acquisition function: the function that determines which input point to measure next
Exploitation: focuses on the vicinity of current best measurement points
Exploration: focuses on unexplored region
Upper confidence bound (UCB): an acquisition function which explicitly specifies the trade-off between exploration and exploitation
-
- β can be increased during the process to avoid sticking in local optimum
Notes: IRM을 사전에 계산한 값이므로, U Σ V 또한 사전에 계산된 값입니다.
Q(z)는 diagonal matrix이므로 서로의 eigenspace에 영향을 주지 않습니다

## Slide 9
Optimization of UED Machine Parameters
20250310 Group Meeting
9
Input points for initial sample dataset will be generated by Latin hypercube sampling(LHS) method
Input parameter: Strength of solenoids, bunch charge, RF gun phase, source beam size
Objective parameter: Beam size, bunch length, normalized emittance, energy spread, q-resolution
R. Preece and J. V. Milanović, IEEE Transactions on Power Systems, vol. 31, no. 2. (2016)

## Slide 10
Optimization of UED Machine Parameters
20250310 Group Meeting
10
Parameter | Range
Charge | [50fC, 100fC]
Source beam size | [20μm, 100μm]
RF gun phase | [-70°, -40°]
Solenoid 1 strength | [0.144T, 0.18T]
Solenoid 2 strength | [0.07664T, 0.0958T]
Automatic General Particle Tracer(GPT) simulation will be conducted by python LUME-GPT module
Number of macroparticles is reduced from 50k to 10k

## Slide 11
Optimization of UED Machine Parameters
20250310 Group Meeting
11
Cavity frequency | 2.856GHz
Gun gradient | 82.84MV/m(max)
Solenoid 1 position | 0.196m
Solenoid 2 position | 1.26m
Aperture position | 0.55m
Aperture diameter | 100μm
Sample position | 1.75m

## Slide 12
Optimization of UED Machine Parameters
20250310 Group Meeting
12
Programming will be based on PyTorch and Xopt library
Surrogate model: Gaussian process
Kernel: Matern function with v=5/2
Initial sample point: 20
Acquisition function: Upper confidence bound hypervolume improvement(UCB-HVI)
- β can be changed for optimization
Number of iteration: 100~500

## Slide 13
Current Progress
20250310 Group Meeting
13
Coding for generation of initial sample dataset(in progress)
Coding for MOBO algorithm(in progress)

## Slide 14
Future Plan
20250310 Group Meeting
14
Completing MOBO algorithm for optimization
Changing some variables in algorithm
(e.g. β, period of optimizing length-scale hyperparameter)
Measurement of hypervolume after rerunning same optimization for several times
Comparing hypervolume with other ML methods (e.g. grid search, MOGA)

## Slide 15
Thank you!
20250310 Group Meeting

## Slide 16
GPT Simulation Code
-PAL-eLabs UED Facility Setup
20250310 Group Meeting
16

## Slide 17
GPT Simulation Code
-PAL-eLabs UED Facility Setup
20250310 Group Meeting
17